## Slide 1
Fleet Analytics • Reliability Engineering • Digital Mine Technologies
Performance Monitoring & Improvement Opportunities in OB & Coal Operations through FMS & FUMS Data
SUMMER INTERNSHIP REPORT · TALABIRA II & III OPEN CAST PROJECT
PRESENTED BY
Sushant Rathore
B.Tech, Mining Engineering (ME'27)
IIT (ISM) Dhanbad
INDUSTRY MENTOR
Nabal Kishor Sharma
Adani Natural Resources | Talabira II & III Open Cast Project | 2026

## Slide 2
INTRODUCTION
Sushant Rathore
Final-year Mining Engineering student with a strong focus on operational data analytics, fleet performance and asset optimization in surface mining.
EDUCATION
B.Tech, Mining Engineering (ME'27)
Indian Institute of Technology (ISM), Dhanbad
INTERNSHIP
Adani Natural Resources
Talabira II & III Open Cast Project
Summer Internship • (2026)
TECHNICAL INTERESTS
Mining Operations & Fleet Performance Analytics
Reliability Engineering & Asset Management
Digital Mining Technologies
Presenter Profile

## Slide 3
Business Context
MINE SNAPSHOT
Talabira II & III OCP
Adani Natural Resources (MDO)
20 MTPA
Normative Capacity
199 HEMM
GPS-Enabled Fleet
Mine Operations Dept.
FMS & FUMS Monitored
DIGITAL MONITORING INFRASTRUCTURE
Fleet Management System (FMS)
Real-time monitoring of fleet operations using GPS and telematics.
Equipment Tracking • Trip Monitoring • Production Monitoring • Equipment Utilization
Fuel Management System (FUMS)
Automated monitoring and management of fuel dispensing.
Fuel Dispensing • Fuel Consumption • Fuel Inventory • Fuel Efficiency
Operational Capabilities
Real-Time Fleet Visibility
Real-time view of equipment location and status.
Production Monitoring
Continuous tracking of output against targets.
Fuel Management
Oversight of consumption and dispensing patterns.
Equipment Utilization
Insight into how effectively assets are used.
Decision Support
Data to guide faster operational choices.
PROJECT RATIONALE
Talabira's FMS and FUMS generate comprehensive operational data across production, fleet operations, and fuel management. While these systems effectively support routine monitoring, their analytical potential offers opportunities for deeper analysis. This project systematically analyses the available data to identify improvement opportunities and propose practical recommendations for enhancing productivity, equipment reliability, and operational decision-making across the mine.

## Slide 4
Project Objectives
PROJECT AIM
To systematically evaluate operational performance at Talabira II & III OCP using FMS and FUMS data, identify improvement opportunities, and develop practical recommendations that enhance productivity, reliability, and operational efficiency.
PROJECT OBJECTIVES
01
Evaluate Fleet Performance
Assess availability, utilization, and reliability across the HEMM fleet.
02
Analyse Production & Fuel Trends
Examine FMS and FUMS data to identify patterns in output and fuel consumption.
03
Identify Improvement Opportunities
Pinpoint gaps in current monitoring and operational practices.
04
Recommend Practical Solutions
Propose data-backed actions to strengthen fleet and production outcomes.
Deliverables
Comprehensive Performance Assessment
A clear picture of current fleet and production performance.
Operational Improvement Opportunities
Specific, evidence-based areas for operational gains.
Data-Driven Recommendations
Actionable proposals grounded in FMS/FUMS analysis.
Enhanced Decision Support
A stronger basis for day-to-day operational decisions.

## Slide 5
Current Operational Workflow
OPERATIONAL DATA FLOW
GPS Satellites
(GNSS Constellation)
Vehicle Tracking Unit
Dashboard & MIS Reports
Central FMS Server
(Data Processing + Analytical)
Cellular Transmission
ROM Coal
(Weighbridge Report)
Operational data is processed into production and performance insights for operational decision-making.
CURRENT SYSTEM CAPABILITIES
Fleet Visibility
Real-time equipment tracking
Production Monitoring
OB & ROM production tracking
Fuel Management
RFID-based fuel monitoring
Performance Reporting
Availability, utilization & MIS reporting
KEY FOCUS AREAS
Production Accuracy
Static Truck Factor estimation
Machine Diagnostics
No integrated machine diagnostics
Equipment Health Monitoring
Limited access to machine health data
Operational Decision Support
Limited real-time operational insights
Ignition
(Wire Sense)
HMR
(Hour Meter Wire)
GPS Position/Speed
Fuel Consumption
(Fuel Report)

## Slide 6
Project Approach & Methodology
EXECUTION TIMELINE
PHASE 1
System
Familiarization
PHASE 2
Stakeholder
Consultation
PHASE 3
Data
Acquisition
PHASE 4
Performance
Analysis
PHASE 5
Opportunity
Identification
PHASE 6
Recommendation
Development
STAKEHOLDER ENGAGEMENT
PRIMARY DATA SOURCES (March – June ‘26)
Mine Operations Team
FMS Operations Team
Survey Department
Project Mentor
Fleet Operations Data
Fuel Consumption Data
Survey & Production Records
Equipment Performance Data

## Slide 7
Fleet Performance Assessment
SUPPORTING PERFORMANCE TRENDS
Chart: 
| March | April | May
Availability | 74.8 | 66.6 | 65.2
Chart: 
| March | April | May
Utilization | 81.9 | 73.8 | 74.2
Equipment Availability
Fleet Utilization
↓ 9.6 percentage point decline during the study period
Lowest utilization recorded in April with partial recovery in May
BREAKDOWN PERFORMANCE
Fleet Breakdown Hours
Chart: 
| March | April | May
Breakdown Hours | 49901 | 59746 | 64333
OPERATIONAL HIGHLIGHTS
NON-OPERATIONAL FLEET
7 → 9 → 14
Machines remained non-operational
BREAKDOWN HOURS
49.9k → 64.3k
≈29% increase over the study period
FLEET PERFORMANCE
Availability ↓ Utilization ↓
Overall fleet performance declined

## Slide 8
Fleet Reliability Assessment
MTBF-MTTR RELIABILITY CLASSIFICATION
Fleet Median: MTBF = 110 hrs | MTTR = 48.2 hrs (193 machines)
Q2
High MTBF + High MTTR
36 Machines (18%)
Reliable, Slow Repair
Q3
Low MTBF + Low MTTR
34 Machines (18%)
Frequent but Fast
← Low MTTR High MTTR →
↑ High
MTBF
↓ Low
MTBF
Q1 — Protect & Benchmark
Replicate maintenance best practices across similar assets.
Q2 — Reduce Repair Time
Improve spare availability and workshop turnaround.
Q3 — Root Cause Analysis
Eliminate recurring failures through preventive maintenance redesign.
Q4 — Immediate Intervention
Prioritize repairs, fast-track spare procurement and evaluate fleet renewal.
IS BREAKDOWN CONCENTRATED? — PARETO ANALYSIS
Top 15 Machines
18.0%
Top 40 Machines
40.8%
Machines contributing 80% BD
56.0%
Remaining Machines
20.0%
KEY RELIABILITY INSIGHT
56% of the fleet contributes to 80% of total breakdown hours, indicating a fleet-wide reliability issue rather than a classical 80/20 concentration.
CRITICAL FLEET
61 Machines
Highest maintenance priority for Q4
PARETO FINDING
56% Fleet → 80% BD Hrs
Broad-based reliability issue

## Slide 9
Production Validation Studies
Bulk Density Assessment
Field measurement of representative mine materials
Engineering Insight
Measured bulk densities varied from 1.10 to 2.60 g/cm³ across mine materials. This significant variation demonstrates that a single static Truck Factor cannot accurately represent all overburden materials, resulting in potential production estimation errors. The findings support the need for material-specific or Dynamic Truck Factors.
Dumper Cycle Time Validation
Field validation of FMS cycle time recording — Komatsu HD785 Dumper
Field Observation
19 min 08 sec
FMS Validated
FMS Record
19 min 05 sec
Validation Finding Manual stopwatch observations differed by only 3 seconds from the FMS record, confirming the accuracy and reliability of FMS cycle time tracking.
Survey Reconciliation
Comparison of FMS-estimated and survey-measured overburden quantity (May 2026)
Survey Measurement
1,616,656 m³
FMS Estimate
1,528,807 m³
Production Deviation: 87,849 m³ (5.43%)
Reconciliation Finding Independent survey measurements recorded 5.43% higher overburden quantity than the FMS estimate. The deviation is primarily attributed to the use of a single static Truck Factor despite varying material densities.

## Slide 10
Operational Improvement Initiatives
Q4 Machine Recovery Programme
30-Day Mandatory Resolution
KEY FINDING
61 machines remained in the critical (Q4) reliability quadrant.
KEY ACTIONS
Machine Classification
Ownership Assignment
Weekly Monitoring
SUCCESS TARGET
61 → <45 Q4 Machines within 90 Days
Failure Code Framework
Maintenance Analytics Enhancement
KEY FINDING
Breakdown hours are recorded without standardized failure-mode classification.
KEY ACTIONS
Standardized Failure Codes
Monthly Analytics Dashboard
Root Cause Analysis
SUCCESS TARGET
Component-Level Diagnostics & PM Optimization
HMR-Based Preventive Maintenance
Ring-Fenced Preventive Maintenance Crew
KEY FINDING
Preventive maintenance is not consistently scheduled using Hour Meter Reading.
KEY ACTIONS
Auto HMR Alerts
Dedicated PM Crew
Compliance Monitoring
SUCCESS TARGET
Reduced Reactive Maintenance & Higher PM Compliance
V-Series Fleet Renewal
Fleet Economic Decision
KEY FINDING
Ageing V-series tippers exhibit persistent failures and prolonged downtime.
KEY ACTIONS
Life Cycle Cost Analysis
Fleet Prioritization
Phased Replacement
SUCCESS TARGET
Improved Fleet Reliability & Lower Lifecycle Cost

## Slide 11
Engineering Solution Frameworks
DYNAMIC TRUCK FACTOR IMPLEMENTATION ROADMAP
Progressive implementation strategy for replacing static OEM Truck Factors with survey-calibrated Dynamic Truck Factors.
Engineering Outcome: Enables progressive reduction in survey frequency while maintaining high FMS production accuracy through Dynamic Truck Factor calibration.
CAN BUS INTEGRATION FRAMEWORK
Machine health monitoring architecture for predictive maintenance and advanced fleet analytics.
Machine
Sensors
Temperature, Pressure, RPM, Fuel Flow, Voltage
→
ECUs
Signal acquisition, diagnostics and fault detection
→
CAN Bus
Network
Communication backbone
→
Telematics
Gateway
CAN aggregation and data transmission
→
Cellular /
Satellite Link
Remote communication with offline buffering
→
FMS Analytics
Dashboard
Real-time monitoring, alerts and predictive analytics
PHASED DEPLOYMENT STRATEGY
Preparation
→
Pilot
→
Alert
Activation
→
Q4
Expansion
→
Fleet
Rollout
→
Continuous
Improvement
Engineering Outcome: Unlocks real-time machine health intelligence, enabling predictive maintenance and data-driven fleet reliability improvement.

## Slide 12
Dynamic Truck Factor — Mathematical Derivation
Engineering derivation of the Dynamic Truck Factor using periodic survey reconciliation.
DEVIATION FACTOR (ε)
ε = (VSurvey − VFMS) / VFMS
ε > 0 → FMS Underestimation → Increase TF ε < 0 → FMS Overestimation → Reduce TF
MATHEMATICAL DERIVATION
VActual = VFMS (1 + ε)
↓
VFMS = TFStatic × NTrips
↓
VActual = TFStatic × NTrips (1 + ε)
↓
Divide both sides by N Trips
↓
TFDynamic = TFStatic (1 + ε)
WORKED EXAMPLE (MAY 2026)
STEP 1 — DEVIATION CALCULATION
ε = (1,616,656 − 1,528,807) / 1,528,807 = 5.75%
→
STEP 2 — MEDIUM DUMPER
TF Dynamic = 26 × (1 + 0.0575) = 27.5 ≈ 27
→
STEP 3 — BIG DUMPER
TF Dynamic = 42 × (1 + 0.0575) = 44.4 ≈ 44
Truck Class
OEM TF
Dynamic TF
Small
13
14
Medium
26
27
Big
42
44

## Slide 13
Business Impact & Expected Benefits
Operational improvements enabled through the proposed recommendations and engineering frameworks.
Production Accuracy
CURRENT STATE
Static Truck Factor
↓
FUTURE STATE
Dynamic Truck Factor
BUSINESS BENEFITS
Higher Accuracy
Reduced Survey Cost
Improved Planning
Maintenance Strategy
CURRENT STATE
Reactive Maintenance
↓
FUTURE STATE
Failure Code + HMR-Based PM
BUSINESS BENEFITS
Reduced Breakdowns
Higher Availability
Better PM Compliance
Fleet Visibility
CURRENT STATE
Limited Machine Visibility
↓
FUTURE STATE
CAN Bus Integration
BUSINESS BENEFITS
Real-Time Monitoring
Early Fault Detection
Faster Decisions
Decision Support
CURRENT STATE
Fragmented Operational Data
↓
FUTURE STATE
Integrated Decision Support
BUSINESS BENEFITS
Data-Driven Decisions
Resource Optimization
Higher Efficiency
OVERALL BUSINESS IMPACT
Together, the proposed operational improvements and engineering frameworks establish a scalable pathway toward safer, more reliable and data-driven fleet operations.

## Slide 14
Towards a Digital Mine
Future technology integration for the next generation Fleet Management System.
Load Management System (LMS)
CURRENT LIMITATION
Static Truck Factors estimate production but cannot measure payload on individual trips.
FUTURE INTEGRATION
Integrate suspension pressure/load sensors with CAN Bus to capture real-time trip-level payload within the existing FMS.
FUTURE VALUE
Real-time payload measurement for highly accurate production reporting.
AI-Based Predictive Maintenance
CURRENT LIMITATION
Maintenance is primarily reactive after faults become visible or failures occur.
FUTURE INTEGRATION
Apply AI/ML models to continuously analyse CAN Bus machine health parameters and identify developing failures before breakdown.
FUTURE VALUE
Predict equipment failures using CAN Bus health data before breakdown occurs.
DIGITAL MINE VISION
Building upon the proposed Dynamic Truck Factor and CAN Bus frameworks, these technologies represent the next step toward a predictive, data-driven Digital Mine at Talabira II & III.

## Slide 15
Key Learnings & Reflections
KEY LEARNINGS
Digital Mine Systems
FMS • FUMS • Telematics • TLS
Operational Analytics
KPI Evaluation • Reliability Analysis
Engineering Solutions
Framework Design • Process Improvement
Industry Exposure
Production • Survey • Fleet operations
CHALLENGES & MITIGATION
Data Quality & Consistency
Validation & Cross-checks
Large–Scale Fleet Data
Structured Analysis
Operational Complexity
Cross-functional Collaboration
Implementation Constraints
Scalable Engineering Solutions
The internship strengthened my ability to transform operational data into practical engineering solutions through structured analysis, field validation, and cross-functional collaboration.

## Slide 16
Industrial Exposure at Talabira II & III OCP
Practical exposure across major opencast mining operations during the internship.
Mine Operations
Production cycle from drilling to overburden and coal extraction.
Drilling & Blasting
Blast design, charging practices and fragmentation assessment.
Loading & Hauling
Excavator–dumper deployment, haul road operations and fleet productivity.
HEMM Maintenance
Workshop practices, preventive maintenance and equipment inspection.
Survey & Drone Mapping
Drone survey, volumetric reconciliation and pit measurements.
Geology & Grade Control
Lithology identification, seam exposure and quality monitoring.
Explosives Management
Explosive magazine, detonators and statutory handling procedures.
Dispatch & Weighbridge
Fleet dispatch, weighbridge operations and production reconciliation.
Mine Safety
Safety committee meetings, field inspections and statutory safety practices.
OVERALL EXPOSURE
Developed a comprehensive understanding of end-to-end opencast mining operations through field exposures, cross-functional interaction and operational observation.

## Slide 17
Mine Visit – Photo Gallery

## Slide 18
Thank You
Questions & Discussion
Enhancing Fleet Monitoring System (FMS)
Through Data-Driven Operational Analysis
Sushant Rathore
Mining Engineering
Indian Institute of Technology (ISM), Dhanbad
Summer Internship — Adani Natural Resources